## Slide 1
Prof. Maulik D. Trivedi
9998265805
maulik.trivedi@darshan.ac.in
2140709
Computer Networks
Unit-1
Introduction to Computer Networks & Internet

## Slide 2: What is Computer Network?
Computer Network is a system in which multiple computers are connected to each other to share information and resources.
Wireless
Wired
Network
Devices
Computers

## Slide 3: Advantages of Computer Network
Better Communication
File Sharing
Entertainment
Flexible Access

## Slide 4: Advantages of Computer Network
Inexpensive System
Instant and Multiple Access
Internet Access
Resource Sharing

## Slide 5: Applications of Computer Network
& Many More….
Business & Finance
Email Services
File & Directory Services
Teleconferencing

## Slide 6: Types of Computer Network
Computer networks can be categories by their size as well as their purpose.
The size of a network can be expressed by the geographic area.
Some of the different networks based on size are:
    Local Area Network - LAN
    Metropolitan Area Network - MAN
    Wide Area Network - WAN

## Slide 7: Local Area Network
A local area network (LAN) is a computer network that interconnects computers within a limited area such as a residence, school, laboratory, university campus or office building.

## Slide 8: Metropolitan Area Network
A metropolitan area network (MAN) is a computer network that interconnects with computer in a metropolitan area like city.
MAN is a larger than LAN but smaller than the area covered by a WAN.
It is also used to interconnection of several local area network.
Navagam
Shapar
Morbi
Rajkot

## Slide 9: Wide Area Network
A wide area network (WAN) is a computer network that exists over a large-scale geographical area.
A WAN connects different networks, including local area networks (LAN) and metropolitan area networks (MAN).
It may be located with in a state or a country or it may be interconnected around the world.
Asia
Africa
America

## Slide 10: Types of Computer Networks - Summary

## Slide 11: Types of Computer Networks - Summary
Basis Of Comparison | LAN | MAN | WAN
Full Name | Local Area Network | Metropolitan Area Network | Wide Area Network
Meaning | A network that connects a group of computers in a small geographical area | It covers relatively large region such as cities, towns | It spans large locality & connects countries together. e.g. Internet
Ownership of Network | Private | Private or Public | Private or Public (VPN)
Design and Maintenance | Easy | Difficult | Difficult
Propagation Delay | Short | Moderate | Long
Speed | High | Moderate | Low
Equipment Used | NIC, Switch, Hub | Modem, Router | Microwave, Radio Transmitter & Receiver
Range(Approximately) | 1 to 10 km | 10 to 100 km | Beyond 100 km
Used for | College, School, Hospital | Small towns, City | State, Country, Continent

## Slide 12: What is Internet?
The internet is a type of world-wide computer network.
The internet is the collection of infinite numbers of connected computers that are spread across the world.
Mobile Network
Global ISP
Regional ISP
Home
Network
Institutional
Network
router
Wired link
wireless
links
smartphone
PC
server
wireless
laptop
Network Components

## Slide 13: Network edge & Network core

## Slide 14: The Network Edge
Computers and other devices are connected at the edge (end) of the network.
These computers are known as hosts or end systems. Router is known as edge router.
mobile network
Global ISP
Regional ISP
Home
Network
Institutional
Network

## Slide 15: Peer to Peer Network
Computers are connected together so that users can share resources and information.
There is no central server for authenticating users, each of them works as both client and server.
e.g. Bit Torrent

## Slide 16: Client – Server Network
Client: Request servers for a task.
  Generally called desktop PCs or workstations.
Server: Receive requests from the clients. Process and response them.
  e.g. Web Server, Email Server

## Slide 17: The Network Core
Defines the connection of different network segments together and process to transmit data packets across the network.
It is implemented through the use of switching techniques.
Switched
Networks
Packet-Switched
Networks
Circuit-Switched
Networks

## Slide 18: Circuit Switched Network
A dedicated channel has to be established before the call is made between users.
The channel is reserved between the users till the connection is active.
For half duplex(one way) communication, one channel is allocated and for full duplex(two way) communication, two channels are allocated.
It is mainly used for voice communication requiring real time services without delay.

## Slide 19: Circuit Switched Network – Cont…
Communication via circuit switching involves three phases:
Circuit Establishment
Data Transfer
Circuit Disconnect

## Slide 20: Packet Switched Network
It is not required to establish the connection initially.
The connection/channel is available to use by users. But when traffic or number of users increases then it will lead to congestion in the network.
Packet switched networks are mainly used for data and voice applications requiring non-real time scenarios.

## Slide 21: Differences
Circuit Switching | Packet Switching
Dedicated path between source and destination | No dedicated path
All packets use same path | Packets travel independently
Reserve the entire bandwidth in advance | Does not reserve bandwidth
Bandwidth wastage | No bandwidth wastage
No store and forward transmission | Supports store and forward transmission

## Slide 22: Switching Network

## Slide 23: Transmission media

## Slide 24: Transmission Media
A transmission media can be defined as any medium that can carry information from a source to a destination.
Transmission Media
Guided Media (Wired)
Unguided Media (Wireless)
Twisted-Pair Cable
Coaxial Cable
Fiber Optic Cable
Radio Wave
Microwave
Infrared Wave

## Slide 25: Guided Media
Guided media are those that provide a wired - channel from one device to another.
Three Guided media commonly used for data transmission are:
Twisted Pair Cable
Coaxial Cable
Fiber Optic Cable

## Slide 26: Twisted Pair Cable
Separately insulated
Twisted together
It is widely used in different kinds of data and voice infrastructure.
The use of two wires twisted together helps to reduce crosstalk and electromagnetic induction.
Two types of twisted pair cable:
UTP
(Unshielded Twisted Pair)
STP
(Shielded Twisted Pair)

## Slide 27: Twisted Pair Cable – Cont…
UTP(Unshielded Twisted Pair)
  Ordinary telephone wires
  Less expensive
  Weak immunity against noise & interferences
  Most used in two categories: Cat-3 & Cat-5
  Used in laboratory
STP(Shielded Twisted Pair)
  An extra metallic shield on each pair
  Relatively more expensive
  Better performance than UTP
  Used in exterior network(outside of building).

## Slide 28: Coaxial Cable
Outer conductor is braided shield
Inner conductor is solid metal
Separated by insulating material, and whole cover by plastic cover
Used in television, long distance telephone transmission
High bandwidth and excellent noise immunity
Outer conductor (shield)
Insulator
Inner Conductor
Plastic cover

## Slide 29: Fiber Optic Cable
Glass or plastic core
Laser or light emitting diode
Small size & weight
Used in high bandwidth network
High data rate & lower attenuation

## Slide 30: Unguided Media
Unguided media transmit electromagnetic waves without using a physical conductor.
This type of communication is often referred to as wireless communication.
  Radio wave
  Microwave
  Infrared Wave

## Slide 31: Radio wave
Highly regulated
Omni directional antennas
Radio waves are used for multicast communications, such as radio and television, and paging systems
Penetrate through walls

## Slide 32: Microwave
Use directional antennas - point to point line of sight communications
Microwave communication
Used for unicast communication such as cellular telephones, satellite networks
Higher frequency ranges cannot efficiently penetrate walls

## Slide 33: Infrared wave
Infrared signals can be used for short-range communication in a closed area using line-of-sight propagation
Used on televisions, VCRs, and stereos all use infrared communication.
Relatively directional
Cheap, easy to build but they do not pass through solid objects

## Slide 34: Network Topologies

## Slide 35: Network Topologies
Network topology is the arrangement of the various components(links, nodes, etc.) of a computer network.
Types of network topologies :
  Bus
  Ring
  Star
  Mesh
  Tree
  Hybrid

## Slide 36: Bus Topology
Every computer and network device is connected to single cable
It transmits data only in one direction
Cost effective
Used in small networks
Easy to expand joining two cables together
It is used in early LAN connection

## Slide 37: Ring Topology
It forms a ring as each computer is connected to another computer, with the last one connected to the first.
Transmission is unidirectional & sequential way that is bit by bit.
Transmitting network is not affected by high traffic or by adding more nodes, as only the nodes having tokens can transmit data.
Cheap to install and expand.

## Slide 38: Star Topology
Computers are connected to a single central hub through a cable.
Fast performance with few nodes and low network traffic.
Easy to troubleshoot & Easy to setup and modify.
Only that node is affected which has failed rest of the nodes can work smoothly.
Hub can be upgraded easily.

## Slide 39: Mesh Topology
Point-to-point connection to other devices or fully connected.
Traffic is carried only between two connected devices.
Robust, costly but not flexible.
Fault is diagnosed easily.
More cable resource used in setup.

## Slide 40: Tree Topology
It has a root node and all other nodes are connected to it forming a hierarchy.
Also called hierarchical topology.
Mostly used in Wide Area Network – WAN.
Expansion of nodes is possible and easy.
Easily managed and maintained.

## Slide 41: Hybrid Topology
A network structure whose design contains more than one topology is said to be hybrid topology.
It is a combination of two or more topologies.
Flexible & reliable as error detection and easy to troubleshoot.
Scalable as size can be increased easily.

## Slide 42: Comparison of Topologies
 | Bus | Ring | Star | Mesh | Tree
Means | every computer and network device is connected to single cable. | Each computer is connected to another, with the last one connected to the first. | All the computers are connected to a single hub through a cable. | All the network nodes are connected to each other. | It has a root node and all other nodes are connected to it forming a hierarchy.
Cost | Average | Cheap | High | High | High
Used in | Small Network | Expand Network | Small Network | Expand Network | Expand Network
Troubleshoot | Easy, But Cables fail then whole network fails. | Difficult; Failure of one computer disturbs the whole network. | Easy; If the hub fails then the whole network is down. | Difficult; Installation and configuration is difficult. | Easy; Central root hub fails, network fails.

## Slide 43: What is Protocol?
Human Protocol(Language)
  “what’s the time?”
  “I have a question”
  Introduction Talk
Network Protocol
  Set of rules
  machines rather than humans
  all communication activity in Internet governed by protocols.
  Protocol is define format, order of message sent and received among network entities, and actions taken on message transmission and reception

## Slide 44: Protocol Layers

## Slide 45: Protocols Layers
To deals with connecting systems that are open for communication with other systems.
OSI Layer Model (Open Systems Interconnection)
Developed by the International Standards Organization (ISO) with seven different layers.
    Physical Layer
    Data Link Layer
    Network Layer
    Transport Layer
    Session Layer
    Presentation Layer
    Application Layer

## Slide 46: Example – Air Plane Travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Departure
Arrival

## Slide 47: How OSI Layer Works?

## Slide 48: Physical Layer
The physical layer is responsible for movements of individual bits from one hop (node) to the next.

## Slide 49: Physical Layer – Cont…
Carries the bit stream over a physical media.
Physical Layer is concerned with:
  Interface and Medium like guided cables
  Representation of bits
  Data rate
  Synchronization of bits
  Line configuration
  Physical topology
  Transmission mode

## Slide 50: Data Link Layer
The data link layer is responsible for moving frames from one hop (node) to the next.

## Slide 51: Data Link Layer – Cont…
Data link layer is concerned with:
  Framing – divide bits stream into data unit (frame)
  Physical addressing
  Flow control – avoid over overwhelming
  Error control – bit loses, retransmission
  Access control

## Slide 52: Network Layer
The network layer is responsible for the delivery of individual packets from the source host to the destination host.

## Slide 53: Network Layer – Cont…
In this layer, packet is combined with header and data.
In case of data link layer, packet delivers on the same network.
If two different networks are connected then packet is concern with network layer.
Network layer is concerned with:
  Logical addressing e.g. 192.168.1.1 (IP Address)
  Routing

## Slide 54: Transport Layer
The transport layer is responsible for the delivery of a message from one process to another.

## Slide 55: Transport Layer – Cont…
This layer ensures that the whole message arrives intact and in order.
Transport layer is concerned with:
  Service-point addressing (port address)
  Segmentation and reassembly
  Connection control
  Flow and error control

## Slide 56: Session Layer
The session layer is responsible for dialog control and synchronization.

## Slide 57: Session Layer – Cont…
This layer is network dialog controller – establishes, maintains, synchronizes the interaction among computers.
Session layer is concerned with:
  Dialog control
  Synchronization

## Slide 58: Presentation Layer
The presentation layer is responsible for translation, compression, and encryption.

## Slide 59: Presentation Layer – Cont…
This layer is concerned with the syntax which refers to order in which data is presented and semantics helps in interpreting a particular pattern.
Presentation layer is responsible for:
  Translation
  Encryption
  Compression

## Slide 60: Application Layer
The application layer is responsible for providing services to the user.

## Slide 61: Application Layer – Cont…
This layer provides various services like:
  Network virtual terminal
  File transfer, access and management
  Mail services
  Directory services

## Slide 62: Summary – OSI Layer
Application
Presentation
Session
Transport
Network
Data link
Physical
To allow access to network resource
To translate, encrypt and compress data
To provide reliable process-to-process message delivery and error recovery
To establish, manage and terminate sessions
To move packets from source to destination; To provide internetworking
To transmit bits over a medium; To provide mechanical & electrical specification
To organize bits into frames; To provide hop-to-hop delivery

## Slide 63: TCP/IP Reference Model (Transmission Control Protocol/Internet Protocol)
It was originally defined as having five layers:
TCP/IP is a set of protocols developed to allow cooperating computers to share resources across the network.
  Application Layer
  Transport Layer
  Network Layer
  Data Link Layer
  Physical Network

## Slide 64: TCP/IP Model Architecture

## Slide 65: Difference
OSI (Open System Interconnection) | TCP/IP (Transmission Control Protocol/ Internet Protocol)
OSI provides layer functioning and also defines functions of all the layers | TCP/IP model is more based on protocols and protocols are not flexible with other layers
In OSI model the transport layer guarantees the delivery of packets | In TCP/IP model the transport layer does not guarantees delivery of packets
Follows horizontal approach | Follows vertical approach
OSI model has a separate presentation layer | TCP/IP doesn’t have a separate presentation layer
OSI is a general model | TCP/IP model cannot be used in any other application
It has 7 layers | It has 5 layers

## Slide 66: Difference - Cont…
OSI (Open System Interconnection) | TCP/IP (Transmission Control Protocol/ Internet Protocol)
Network layer of OSI model provide both connection oriented and connectionless service | The Network layer in TCP/IP model provides connectionless service
OSI model has a problem of fitting the protocols in the model | TCP/IP model does not fit any protocol
Protocols are hidden in OSI model and are easily replaced as the technology changes | In TCP/IP, replacing protocol is not easy
OSI model defines services, interfaces and protocols very clearly and makes clear distinction between them | In TCP/IP, it is not clearly separated its services, interfaces and protocols

## Slide 67: Protocol Layers: Summary

## Slide 68: Delay, Loss & Throughput
Delay
  As a packet travels from one node (host or router) to the subsequent node (host or router) along this path, the packet suffers from several types of delays at each node along the path.
  Where
dnodal = dproc + dqueue + dtran + dprop
dnodal | = | Total Delay
dproc | = | Processing Delay
dqueue | = | Queuing Delay
dtran | = | Transmission Delay
dprop | = | Propagation Delay

## Slide 69: Delay – Cont…
Processing Delay (dproc)
  The time required to examine the packets header and determine where to direct the packet.
  To check bit level error
  Determine output link
  Delay in terms of microseconds

## Slide 70: Delay – Cont…
Queuing Delay (dqueue)
  A time to wait at output link for transmission.
  Depends on congestion level of router.
  If queue is empty then delay will be zero.
  If queue is full (heavy traffic) then delay will be long.
  Delay in terms of micro second to millisecond.

## Slide 71: Delay – Cont…
Transmission Delay (dtran = L/R)
  An amount of time required for the router to transmit the packet.
  Its depends on packet length(L) and transmission rate(R) of link.

## Slide 72: Delay – Cont…
Propagation Delay (dprop= d/s)
  A time required to propagate from the beginning of the link to router B.
  Depends on the length of physical medium(d) link and propagation speed(s) of link
  Delay in terms of millisecond.

## Slide 73: Packet Loss
Packet loss is the failure of one or more transmitted packets to arrive at their destination.
The loss of data packets depends on the switch queue/buffer. The loss of data packets increases with the increases in the traffic intensity.
It affects the performance
  of the network.

## Slide 74: Throughput
Throughput or Network Throughput is the rate of successful message delivery over a communication channel.
Throughput is measured in bits(data) per second (bit/s or bps)
server, with
file of F bits
send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
Client

## Slide 75: History of Computer Networks
1961-1972 : The development of Packet Switching
1972-1980 : Proprietary Network and Internetworking
1980-1990 : A Proliferation of Networks
1990s : The Internet Explosion
Recent Developments…

## Slide 76: Outline - Revised
What is Computer Network? Connected each other
Advantages of Computer Network
Applications of Computer Network
Type of Computer Network LAN, MAN, WAN
What is Internet? Infinite nos. of connected computers across the world
What is Protocol? Set of Rules
The Network Edge Host-end system & edge router
The Network Core Circuit Switched & Packet Switched
Transmission Media Guided- Wired & Unguided-Wireless
Network Topologies Bus, Ring, Star, Mesh, Tree, & Hybrid
Protocol Layers OSI Layer & TCP/IP Layer
Delay, Loss & Throughput

## Slide 77
Thank You